RTCD137  SERIES　　　（ 85℃ 5000H）

●Compliant to the RoHS directive.

●Long-life and high-ripple series for solar photovoltaic grid-connected

inverter realized through adoption of high-reliability organic acid type

electrolyte liquid and improvement of etched foil technology for high

voltage and manufacturing process.

■Product Specifications

| (unit: mm) | Items | Specifications |
| --- | --- | --- |
|  | Temperature range | -40℃～+85℃ |
|  | Rated voltage | 350～450V.DC |
|  | Capacitance tolerance | ±20% (20℃, 120Hz) |
|  | Leakage current | 0.01CV (μA)or 5mA,whichever is smaller |
|  |  | [C=nominal capacitance (μF),V= rated voltage (V)] |
|  | Dissipation factor | Less than the value specified in the standard products table. |
|  | Permissible ripple current | As specified in the standard products table. (85℃, 120Hz) |
|  | High-temperature load | After the rated voltage with specified ripple current is applied at 85℃ for 2000 hours : Capacitance tolerance : ±20% or less of the initial value Dissipation factor : 200% or less of the specified initial value Leakage current : Specified initial value or less |
| ΦD | P | S | T | Cap material |  |  |  |
| 51 | 22.0 | M5×10 | 5.5 | Phenol |  |  |  |
| 64 | 28.6 | M5×10 | 5.5 | Phenol |  |  |  |
| 77 | 32.0 | M5×10 | 4.5 | Phenol |  |  |  |
| 90 | 32.0 | M5×10 | 4.0 | Phenol |  | Standard | JIS C 5101-4 |

| Ripple current correction coefficient |  | Part number(Example): RTCD137 400V 10,000μF±20% F case（Φ90mm）product |
| --- | --- | --- |
| Temperature (℃) | 40 | 60 | 85 |  |  |  | RTCD137 2G 103 Y F 157 M D 5 Series Voltage Code Capacitance code Mounting style Diameter code Length Cap. tolerance Diameter Terminal Type of screw |
| Coefficient | 1.89 | 1.67 | 1.0 |  |  |  |  |
| Frequency (Hz) | 50/60 | 120 | 300 | 1K | ≥10K |  |  |
| Coefficient | 0.7 | 1.0 | 1.1 | 1.3 | 1.4 |  |  |

■Standard Products Table

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 85℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 350 2V (400) | 1200 | 51×75 | 0.15 | 5.5 | 85 | 88 | RTCD1372V122YC075M |
|  | 1500 | 51×75 | 0.15 | 6.1 | 68 | 70 | RTCD1372V152YC075M |
|  | 1800 | 51×96 | 0.15 | 7.4 | 57 | 59 | RTCD1372V182YC096M |
|  | 2200 | 51×96 | 0.15 | 8.2 | 46 | 48 | RTCD1372V222YC096M |
|  | 2700 | 51×130 | 0.15 | 10.2 | 38 | 40 | RTCD1372V272YC130M |
|  | 3300 | 51×130 | 0.15 | 11.3 | 30 | 32 | RTCD1372V332YC130M |
|  | 3900 | 64×115 | 0.15 | 12.8 | 26 | 28 | RTCD1372V392YD115M |
|  | 4700 | 64×130 | 0.15 | 14.8 | 21 | 22 | RTCD1372V472YD130M |
|  | 5600 | 64×155 | 0.15 | 17.3 | 18 | 19 | RTCD1372V562YD155M |
|  |  | 77×115 | 0.15 | 16.3 | 18 | 19 | RTCD1372V562YE115M |
|  | 6800 | 64×195 | 0.15 | 21.1 | 15 | 15 | RTCD1372V682YD195M |
|  |  | 77×130 | 0.15 | 18.8 | 15 | 15 | RTCD1372V682YE130M |
|  | 8200 | 77×155 | 0.15 | 22.1 | 12 | 15 | RTCD1372V822YE155M |
|  | 10000 | 90×157 | 0.15 | 25.9 | 10 | 15 | RTCD1372V103YF157M |
|  | 12000 | 90×157 | 0.15 | 28.4 | 8 | 13 | RTCD1372V123YF157M |
|  | 15000 | 90×196 | 0.15 | 34.6 | 7 | 10 | RTCD1372V153YF196M |
|  | 18000 | 90×236 | 0.15 | 41.1 | 7 | 10 | RTCD1372V183YF236M |
| 400 2G (450) | 1000 | 51×75 | 0.15 | 5.0 | 102 | 105 | RTCD1372G102YC075M |
|  | 1200 | 51×75 | 0.15 | 5.5 | 85 | 88 | RTCD1372G122YC075M |
|  | 1500 | 51×96 | 0.15 | 6.7 | 68 | 70 | RTCD1372G152YC096M |
|  | 1800 | 51×96 | 0.15 | 7.4 | 57 | 58 | RTCD1372G182YC096M |
|  | 2200 | 51×130 | 0.15 | 9.2 | 46 | 48 | RTCD1372G222YC130M |
|  | 2700 | 64×96 | 0.15 | 9.9 | 38 | 40 | RTCD1372G272YD096M |
|  | 3300 | 64×115 | 0.15 | 11.8 | 30 | 32 | RTCD1372G332YD115M |
|  | 3900 | 64×130 | 0.15 | 13.5 | 26 | 28 | RTCD1372G392YD130M |
|  | 4700 | 64×155 | 0.15 | 15.9 | 21 | 22 | RTCD1372G472YD155M |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 40℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 400 2G (450) | 4700 | 64×155 | 0.15 | 15.9 | 21 | 22 | RTCD1372G472YD155M |
|  | 4700 | 77×115 | 0.15 | 14.9 | 21 | 22 | RTCD1372G472YE115M |
|  | 5600 | 64×195 | 0.15 | 19.1 | 18 | 19 | RTCD1372G562YD195M |
|  | 5600 | 77×130 | 0.15 | 17.0 | 18 | 19 | RTCD1372G562YE130M |
|  | 6800 | 77×155 | 0.15 | 20.2 | 15 | 15 | RTCD1372G682YE155M |
|  | 8200 | 90×157 | 0.15 | 23.5 | 12 | 15 | RTCD1372G822YF157M |
|  | 10000 | 90×157 | 0.15 | 25.9 | 10 | 15 | RTCD1372G103YF157M |
|  | 12000 | 90×196 | 0.15 | 31.0 | 8 | 13 | RTCD1372G123YF196M |
|  | 15000 | 90×236 | 0.15 | 37.5 | 8 | 10 | RTCD1372G153YF236M |
| 450 2W (500) | 1000 | 51×75 | 0.15 | 5.0 | 102 | 105 | RTCD1372W102YC075M |
|  | 1200 | 51×96 | 0.15 | 6.0 | 85 | 88 | RTCD1372W122YC096M |
|  | 1500 | 51×115 | 0.15 | 7.2 | 68 | 70 | RTCD1372W152YC115M |
|  | 1800 | 51×130 | 0.15 | 8.3 | 56 | 58 | RTCD1372W182YC130M |
|  | 2200 | 64×96 | 0.15 | 9.0 | 46 | 48 | RTCD1372W222YD096M |
|  | 2700 | 64×115 | 0.15 | 10.7 | 38 | 40 | RTCD1372W272YD115M |
|  | 3300 | 64×130 | 0.15 | 12.4 | 30 | 35 | RTCD1372W332YD130M |
|  | 3900 | 64×155 | 0.15 | 14.5 | 27 | 32 | RTCD1372W392YD155M |
|  | 3900 | 77×115 | 0.15 | 13.6 | 27 | 32 | RTCD1372W392YE115M |
|  | 4700 | 64×195 | 0.15 | 17.5 | 21 | 21 | RTCD1372W472YD195M |
|  | 4700 | 77×130 | 0.15 | 15.6 | 21 | 21 | RTCD1372W472YE130M |
|  | 5600 | 77×155 | 0.15 | 18.3 | 20 | 20 | RTCD1372W562YE155M |
|  | 6800 | 90×157 | 0.15 | 21.4 | 18 | 18 | RTCD1372W682YF157M |
|  | 8200 | 90×157 | 0.15 | 23.5 | 15 | 15 | RTCD1372W822YF157M |
|  | 10000 | 90×196 | 0.15 | 28.3 | 12 | 15 | RTCD1372W103YF196M |
|  | 12000 | 90×236 | 0.15 | 33.6 | 9 | 12 | RTCD1372W123YF236M |